## Slide 1: Module 9: Network Security Appliances and Technologies
CompTIA Security+ Guide
to Network Security Fundamentals, 7th Edition

## Slide 2: Module Objectives
By the end of this module, you should be able to:
1. List the different types of network security appliances and how they can be used
2. Describe network security technologies

## Slide 3: Security Appliances
Security can be achieved through appliances that directly address security and by using the security features in standard networking devices
Using both standard networking devices and security appliances can result in a layered security approach
Appliances include:
  Firewalls
  Proxy servers
  Deception instruments
  Intrusion detection and prevention systems
  Network hardware security models

## Slide 4: Firewalls (1 of 6)
To use firewalls effectively, you must understand the function of firewalls and know the different types of firewalls and specialized firewall appliances
Firewall Functions
  A firewall uses bidirectional inspection to examine outgoing and incoming packets
  The actions are based on specific criteria or rules (called rule-based firewalls)
  A more flexible type of firewall is a policy-based firewall which allows more generic statements instead of specific rules
  Firewalls can also apply content/URL filtering

## Slide 5: Firewalls (2 of 6)

## Slide 6: Firewalls (3 of 6)
Firewall Categories
  Stateful vs. stateless
  Open source vs. proprietary
  Hardware vs. software
  Host vs. appliance vs. virtual

## Slide 7: Firewalls (4 of 6)

## Slide 8: Firewalls (5 of 6)

## Slide 9: Firewalls (6 of 6)
Specialized Firewall Appliances
  Web application firewall
  Network address translation gateway
    Network address translation (NAT) is a technique that allows private IP addresses to be used on the public internet
  Next generation firewall
  Unified threat management (UTM)
    UTM is a device that combines several security functions such as packet filtering, antispam, antiphishing, antispyware, encryption, intrusion protection, and web filtering

## Slide 10: Proxy Servers (1 of 2)
Proxies are devices that act as substitutes on behalf of the primary device
A forward proxy is a computer or an application that intercepts user requests from the internal secure network and processes the requests on behalf of the user
A reverse proxy routes requests coming from an external network to the correct internal server
A proxy server can provide a degree of protection
  It can look for malware by intercepting it before it reaches the internal endpoint
  It can hide the IP address of endpoints inside the secure network so that only the proxy server’s IP address is used on the open Internet

## Slide 11: Proxy Servers (2 of 2)

## Slide 12: Deception Instruments (1 of 3)
Deception can be used as a security defense
  By directing threat actors away from a valuable asset to something that has little or no value
Network deception can involve creating and using honeypots and sinkholes
Honeypots
  A honeypot is a computer located in an area with limited security that serves as “bait” to threat actors
  Two goals of using a honeypot:
    Deflect
    Discover

## Slide 13: Deception Instruments (2 of 3)
Figure 9-6 Honeypot dashboard

## Slide 14: Deception Instruments (3 of 3)
Honeypots (continued)
  Different types of honeypots:
    A low-interaction honeypot may only contain a login prompt
    A high-interaction honeypot is designed for capturing more information from the threat actor
      This type of honeypot can collect information from threat actors about attack techniques or the particular information they are seeking from the organization
  A honeynet is a network of honeypots set up with intentional vulnerabilities
Sinkholes
  A sinkhole is a “bottomless pit” designed to steer unwanted traffic away from its intended destination to another device
    The goal is to deceive the threat actor into thinking the attack was successful

## Slide 15: Intrusion Detection and Prevention Systems (1 of 3)
An intrusion detection system (IDS) can detect an attack as it occurs
An intrusion prevention system (IPS) attempts to block the attack
Inline system is connected directly to the network and monitors the flow of data as it occurs
A passive system is connected to a port on a switch, which receives a copy of network traffic
IDS systems can be managed in different ways:
  In-band management is through the network itself by using network protocols and tools
  Out-of-band management is using an independent and dedicated channel to reach the device

## Slide 16: Intrusion Detection and Prevention Systems (2 of 3)
Monitoring Methodologies
  Anomaly-based monitoring compares current detected behavior with baseline
  Signature-based monitoring looks for well-known attack signature patterns
  Behavior-based monitoring detects abnormal actions by processes or programs
    Alerts user who decides whether to allow or block activity
  Heuristic monitoring uses experience-based techniques
    Attempts to answer the question “Will this do something harmful if it is allowed to execute?”

## Slide 17: Intrusion Detection and Prevention Systems (3 of 3)
A network intrusion detection system (NIDS) watches for attacks on the network
  NIDS sensors installed on firewalls and routers gather information and report back to central device
A network intrusion prevention system (NIPS) monitors to detect malicious activities and also attempts to stop them

## Slide 18: Network Hardware Security Modules
A hardware security module (HSM) is a removable external cryptographic device
For endpoints, an HSM is typically a USB device, an expansion card, or a device that connects directly to a computer through a port
A network hardware security module performs cryptographic operations such as key management, key exchange, onboard random number generation, key storage facility, and accelerated symmetric and asymmetric encryption

## Slide 19: Configuration Management
It is essential that security appliances be properly configured
Basic configuration management tools include:
  Secure baseline configurations
  Standard naming conventions
  Defined Internet Protocol schema
  Diagrams

## Slide 20: Knowledge Check Activity 1
Which of the following network security devices is a computer that is purposely located in an area with limited security to attract threat actors?
  a. Forward proxy
  b. Honeypot
  c. Inline system
  d. Behavior monitor

## Slide 21: Knowledge Check Activity 1: Answer
Which of the following network security devices is a computer that is purposely located in an area with limited security to attract threat actors?
  Answer: b. Honeypot
  A honeypot is a computer located in an area with limited security that serves as “bait” to threat actors. Its purpose is to deflect and discover threats.

## Slide 22: Security Technologies
There are general security technologies that can provide a defense
Some of these technologies can be found in both standard networking devices (switches and routers) and specialized security appliances
Categories of security technologies include:
  Access technologies
  Monitoring and managing technologies
  Design technologies

## Slide 23: Access Technologies (1 of 7)
Access Control List (ACL)
  An access control list (ACL) contains rules that administer the availability of digital assets by granting or denying access to the assets
  Two types of ACLS include:
    Filesystem ACLs filter access to files and directories on an endpoint by telling the OS who can access the device and what privileges they are allowed
    Networking ACLs filter access to a network
      Often found on routers
  Router ACLs can be used on external routers to restrict vulnerable protocols and limit traffic from entering the network
  Internal router ACLs are often configured with explicit allow and deny statements for specific addresses and protocol services

## Slide 24: Access Technologies (2 of 7)
Virtual Private Network (VPN)
  A VPN is a security technology that enables authorized users to use an unsecured public network (the Internet) as if it were a secure private network
  Two common types of VPNs:
    A remote access VPN
    A site-to-site VPN
  A full tunnel sends all traffic to the VPN concentrator and protects it
  A split tunnel routes only some traffic over the secure VPN while other traffic directly accesses the Internet (this helps preserve bandwidth)
  The most common protocols used for VPNs are IPsec and SSL

## Slide 25: Access Technologies (3 of 7)
Network Access Control (NAC)
  NAC examines the current state of a system or network device before it can connect to the network
  Any device that does not meet a specified set of criteria can connect only to a “quarantine” network where the security deficiencies are corrected
  NAC uses software “agents” to gather information and report back (called host agent health checks)
  An agent may be a permanent NAC agent or a dissolvable NAC agent that disappears after reporting information to the NAC
  The NAC technology can be embedded within a Microsoft Windows Active Directory (AD) domain controller
    NAC uses AD to scan the device (called agentless NAC)

## Slide 26: Access Technologies (4 of 7)

## Slide 27: Access Technologies (5 of 7)
Data Loss Prevention
  DLP is considered as rights management, or the authority of the owner of the data to impose restrictions on its use
  DLP is a system of security tools that is used to recognize and identify data that is critical to the organization
  Most DLP systems use content inspection which is defined as a security analysis of the transaction within its approved context
  An administrator creates DLP rules based on the data and the policy
  These rules are loaded into a DLP server
  When a policy violation is detected by the DLP agent it is reported back to the DLP server

## Slide 28: Access Technologies (6 of 7)
Data Loss Prevention (continued)
  When a server is notified of a policy violation different actions can be taken:
    Block the data
    Redirect it to an individual who can examine the request
    Quarantine the data until later
    Alert a supervisor of the request
  A process called tokenization obfuscates sensitive data elements, such as an account number, into a random string of characters (token)
    The original sensitive data element and the token are stored in a database called a token vault so that if the actual data element is needed, it can be retrieved as needed
    Tokenization is illustrated in Figure 9-8 on the following slide

## Slide 29: Access Technologies (7 of 7)
Figure 9-8 Tokenization

## Slide 30: Technologies for Monitoring and Managing (1 of 6)
Port Security
  Threat actors who access a network device through an unprotected port can reconfigure the device to their advantage
  Route security is the trust of packets sent through a router
    False route information can be injected or altered by weak port security
  Broadcast storm prevention can be accomplished by loop prevention
    Loop prevention uses the IEEE 802.1d standard spanning-tree protocol (STP)
    STP uses an algorithm that creates a hierarchical tree layout that spans the entire network

## Slide 31: Technologies for Monitoring and Managing (2 of 6)
Figure 9-9 Broadcast storm

## Slide 32: Technologies for Monitoring and Managing (3 of 6)
Packet Capture and Analysis
  Analyzing packets helps to monitor network performance and reveal cybersecurity incidents
  Monitoring traffic on switches can be done in two ways:
    A separate port TAP (test access point) can be installed
    Port mirroring (also called port spanning) allows the administrator to configure the switch to copy traffic on some or all ports to a designated monitoring port on the switch
Monitoring Services
  An external third-party monitoring service can be used to provide additional resources to assist an organization in its cybersecurity defenses

## Slide 33: Technologies for Monitoring and Managing (4 of 6)
Figure 9-10 Port TAP

## Slide 34: Technologies for Monitoring and Managing (5 of 6)
Figure 9-11 Port Mirroring

## Slide 35: Technologies for Monitoring and Managing (6 of 6)
File Integrity Monitors
  File integrity monitors examine files to see if they have changed
  File integrity monitors are used for detecting malware as well as maintaining compliance with industry-specific regulations
Quality of Service (QoS)
  QoS is a set of network technologies used to guarantee its ability to dependably serve network resources and high-priority applications to endpoints
  A network administrator can assign the order in which packets are handled and the amount of bandwidth given to an application or traffic flow (called traffic shaping)
  Almost all firewalls today recognize QoS settings

## Slide 36: Design Technologies (1 of 7)
Network Segmentation
  Examples of network segmentation include virtual LANs and a demilitarized zone
  Zero trust is a strategic initiative about networks that is designed to prevent successful attacks
    It attempts to eliminate the concept of trust from an organization’s network architecture
  Zero trust requires that networks be segmented
  A network can be segmented by separating devices into logical groups by creating a virtual LAN (VLAN)
  VLANs can be isolated so that sensitive data is transported only to members of the VLAN

## Slide 37: Design Technologies (2 of 7)
Network Segmentation (continued)
  A demilitarized zone (DMZ) is a separate network located outside secure network perimeter
  Untrusted outside users can access DMZ but cannot enter the secure network
  A common approach to configuring a DMZ is to use a jump box (sometimes called a jump server or jump host)
    A jump box is a minimally configured administrator server that connects two dissimilar security zones while providing tightly restricted access between them

## Slide 38: Design Technologies (3 of 7)

## Slide 39: Design Technologies (4 of 7)

## Slide 40: Design Technologies (5 of 7)
Load Balancing
  Load balancing is a technology that can help to evenly distribute work across a network and can allocate requests among multiple devices
  Advantages of load-balancing technology:
    Reduces probability of overloading a single server
    Optimizes bandwidth of network computers
  Load balancing is achieved through software or hardware device (load balancer)
  Different scheduling protocols used in load balancers:
    Round-robin
    Affinity

## Slide 41: Design Technologies (6 of 7)
Load Balancing (continued)
  When multiple load balancers are used together, they can be placed in different configurations that include:
    In an active-passive configuration, the primary load balancer distributes the network traffic to the most suitable server, while the secondary load balancer operates in a “listening mode”
    In an active-active configuration, all load balancers are always active
  Load balancing can also support session persistence, which is a process in which a load balancer creates a link between an endpoint and a specific network server for the duration of a session
    This can help improve the user experience and optimize network resource usage

## Slide 42: Design Technologies (7 of 7)
Load Balancing (continued)
  Security advantages of using a load balancer:
    They can detect and stop attacks directed at a server or application
    Can also detect and prevent protocol attacks
    Some load balancers can hide HTTP error pages or remove server identification headers from HTTP responses, denying attackers additional information about the internal network

## Slide 43: Knowledge Check Activity 2
What type of access technology routes some traffic over a secure VPN while other traffic accesses the Internet directly without going through the VPN?
  a. Split tunnel
  b. Site-site VPN
  c. Router ACL
  d. Full tunnel

## Slide 44: Knowledge Check Activity 2: Answer
What type of access technology routes some traffic over a secure VPN while other traffic accesses the Internet directly without going through the VPN?
  Answer: a. Split tunnel
  A split tunnel routes only some traffic over the secure VPN while other traffic directly accesses the Internet (this helps preserve bandwidth).

## Slide 45: Self-Assessment
Consider the network security appliances and technologies you have studied in this module. Based on what you know now, if you could pick only one network security appliance and one security technology you could deploy on a network you were managing, which would they be and why?

## Slide 46: Summary (1 of 2)
A computer firewall is designed to limit the spread of malware
Stateless packet filtering on a firewall looks at a packet and permits or denies it based solely on the firewall rules
  Stateful packet filtering uses both the firewall rules and the state of the connection
There are several specialized firewall appliances: a web application firewall (WAF), a next generation firewall (NGFW), unified threat management (UTM) device
A forward proxy is a computer or program that intercepts user requests from the internal network and processes these requests on behalf of the user
A honeypot is a computer located in an area with limited security that serves as “bait” to threat actors
An intrusion detection system (IDS) can detect an attack as it occurs, an intrusion prevention system (IPS) attempts to block the attack

## Slide 47: Summary (2 of 2)
A network hardware security module is a special trusted network computer that performs cryptographic operations such as key management, key exchange, onboard random number generation, key storage facility, and symmetric and asymmetric encryption
An access control list (ACL) contains rules that administer the availability of digital assets by granting or denying access to the assets
Network access control (NAC) examines the current state of an endpoint before it can connect to the network
Data loss prevention (DLP) is a system of security tools used to recognize and identify data critical to the organization and ensure that it is protected
Broadcast storm prevention can be accomplished by loop prevention, which uses the IEEE 802.1d standard spanning-tree protocol (STP)